## Slide 1: N-FEE | F-FEE Comparison
URD | ICD Overview

## Slide 2: Base Information

## Slide 3: Documents Evaluated
LESIA
DLR
URD
ICD
Evaluation Premises
The development head is the LESIA solution.
  If the requirement is listed in both versions of the documents, is understood that LESIA SW will have it first, with no development impact for DLR.
Inclusion or deletion of MEB or FEE modes impact directly the data source (NUC).
  The SW impact in these cases will be considered as “low”, as this kind of change was already implemented in the last delivery (R1+)
ICD was reviewed as a concept (not requirement by requirement), due to its characteristics:
  The RMAP Map is implemented and managed by R. França – No impact in SW
  The SW change needed after a RMAP Map change will be considered as “low”, as this kind of change was already implemented in the last delivery (R1+)

## Slide 4: LESIA Architecture (V2)

## Slide 5: DLR Architecture (V2 based)
DEB
AEB1
AEB2
AEBN
SYNC

## Slide 6: “ICD”s Comparison

## Slide 7: State Machine Comparison:
Considerations:
State machines walkthrough is different between N-FEE and F-FEE
  In F-FEE is possible to access pattern modes from Stand By state – This is not permitted for N-FEE (only from ON state)
  F-FEE State “INIT” is not defined in N-FEE State Machine
  F-FEE State “Test Partial R/O”” is not defined in N-FEE State Machine
  N-FEE States “Trap Pumps” are not defined in F-FEE State Machine
Inconsistencies between F-FEE ICD info and URD info regarding F-FEE state machine
  There’s no Test Partial Readout mode in the F-FEE URD description
There’s no correlation between AEB State Machine (and AEB itself ) between N-FEE and F-FEE
LESIA
DLR

## Slide 8: RMAP Commands Implementation
Command acronym (F-FEE) | Description | Functional (Y/N) | Implemented (Y/N)
DTC_AEB_ONOFF | Command sets state of 1 to 4 VDIG on/off switches. | Y | Partial (Only reply, no function implemented)
DTC_PLL_REG | Command uploads content of PLL controller registers REG_ID. | N | ?
DTC_WDW_TABLE | Command uploads content of window coordinate table. | Y | N
DTC_WDW_IDX | Command set index and length of window list for AEB i. | Y | N
DTC_TMOD_CONF | Command configures test mode. | - | Not Defined (Place Holder for future needs)
DTC_FEE_MOD | Command sets operating mode the F-FEE | Y | Y
DTC_IN_MOD | Command selects the input for DEB window processing for the eight data processing channels. | Y | Partial (NO DATA not implemented)
DTC_WDW_SIZ | Command sets X & Y window size. | Y | N
DTC_PRO_MOD | Command sets DEB processing mode. | - | Command discarted
DTC_OVS_LIN | Command sets overscan line number for AEB i. | Y | To be written
DTC_OVS_PIX | Command sets overscan pixel number for AEB i. | - | Command discarted
DTC_TRG_25S | Command trigs detector ‘25S_N_CYC’ detector readout sequences. | Y | N
DTC_SEL_TRG | Command selects the source for the 2.5s signal sync. | Y | Partial (Only reply, no function implemented)
DTC_25S_DLY | Command sets delay between reception of 2.5s sync pulse and effective start of detector readout sequence. Delay parameter is expressed in 50 MHz clock periods | Y | Partial (Only reply, no function implemented)
DTC_FRM_CNT | Command presets the content of the frame counters. | Y | N
DTC_SEL_SYN | Command selects the input (main or redundant) for the 50 MHz sync. clock and the 2.5s sync. signal. | Y | Partial (Only reply, no function implemented)
DTC_RST_CPS | Command resets data processing counters / pointers and status. | N | To be written
DTC_RST_WDG | Command resets watchdog activation flag. | N | To be written
DTC_DEB_HK | Command requests DEB housekeeping packet. | Y | N

## Slide 9: RMAP Commands Implementation
Command acronym | Description | Functional (Y/N) | Implemented (Y/N)
ATC_RESET | Resets the AEB FPGA. | Y | N
ATC_CTRL_STATE | Set the AEB FPGA state | Y | Partial (Only reply, no function implemented)
ATC_CTRL_DAC | Triggers a write access to the AEB DACs. The configuration of the DACs is setvia ATC_SET_DAC1 and ATC_SET_DAC2. | N | ?
ATC_CTRL_ADC | Triggers a read or write access to the AEB’s ADC configuration or a read command to start the ADC’s conversion. The configuration of the ADCs is set via ATC_SET and ATC_SET_ADC2 | N | ?
ATC_CTRL_VASP | Triggers a read or access to the AEB’s configuration or starts VASP-internal auto calibration. | N | ?
ATC_SET_PATTERN | Sets the configuration of the AEB-FPGA-internal SimuCam Pattern Generator. | Y | N
ATC_SET_SEQ | Sets the configuration of AEB-FPGA-internal sequencer. | N | ?
ATC_SET_DAC1 | Set the configuration of the AEB DACs to configure Vog and Vrd. | N | ?
ATC_SET_DAC2 | Set the configuration of the AEB DACs to configure Vod. | N | ?
ATC_SET_AEB | Sets the configuration of the AEB-FPGA. | Y | N
ATC_SET_KEY | Sets a configuration key to unlock access or activate the functionality configured via ATC_SET_AIT1 and ATC_SET_AIT2. | N | ?
ATC_SET_AIT1 | For DLR-internal AIT. | N | ?
ATC_SET_AIT2 | For DLR-internal AIT. | N | ?
ATC_SET_ADC1 | Set the configuration of the AEB ADC1. | N | ?
ATC_SET_ADC2 | Set the configuration of the AEB ADC2. | N | ?
ATC_GET_VASP_CFG | Reads the VASP configuration register triggered by and read after ATC_CTRL_VASP from the AEB HK register. | N | ?
ATC_GET_ADC1_CFG | Reads the ADC1 configuration register triggered by and read after ATC_CTRL_ADC from the AEB HK register. | N | ?
ATC_GET_ADC2_CFG | Reads the ADC2 configuration register triggered by and read after ATC_CTRL_ADC from the AEB HK register. | N | ?
ATC_GET_HK | Reads the (complete) AEB HK register. | N | ?

## Slide 10: URD Comparison

## Slide 11: URD Comparison: N-FEE x F-FEE
# | DLR URD Section | LESIA URD Section | Comparison
1 | General Requirements | SimuCam general requirements | Same Content ¦ No changes needed
2 | Software Requirements | SimuCam SSW requirements | -
 | General Software Requirements |  | Same Content ¦ No changes needed
3 | MEB General Requirements | SimuCam MEB general requirements | 
3.1 | MEB Communication Interface | MEB communication interface | DLR: Establishes the Services that should be implemented. Needs to be evaluated, but should not be a problem, as the PUS DB is defined by DLR, reviewed by IMT and forwarded to LESIA.
 | MEB Modes | MEB Modes | Same Content ¦ No changes needed
3.2 | F-FEE Emulation Entities | N-FEE simulation entities | DLR: SimuCam should manage 2 F-FFE ¦ 4 SpW links associated to 1 F-FEE F-FEE states: FFEE_CONFIG; FFEE_RUNNING_STANDBY;FFEE_RUNNING_IMAGE ; FFEE_RUNNING_WINDOW ; FFEE_RUNNING_IMAGE_INTERACTIVE; FFEE_RUNNING_WINDOW_INTERACTIVE ; FFEE_RUNNING_IMAGE_TEST ; FFEE_RUNNING_WINDOW_TEST LESIA: SimuCam should manage 6 N-FEE ¦ 1 SpW links associated to 1 F-FEE N-FEE states: NFEE_CONFIG; NFEE_RUNNING_ON; NFEE_RUNNING_STANDBY; NFEE_RUNNING_FULLIMAGE; NFEE_RUNNING_WINDOWING; NFEE_RUNNING_FULLIMAGE_PATTERN; ; NFEE_RUNNING_WINDOWING_PATTERN; NFEE_RUNNING_PARALLEL_TRAP_PUMP_1; NFEE_RUNNING_PARALLEL_TRAP_PUMP_2; NFEE_RUNNING_SERIAL_TRAP_PUMP_1; NFEE_RUNNING_SERIAL_TRAP_PUMP_2

## Slide 12: URD Comparison: N-FEE x F-FEE
# | DLR URD Section | LESIA URD Section | Comparison
 | Reset and Start-up | Reset and startup | Same Content ¦ No changes needed
 | Non-Volatile Memory | Non-volatile memory | Same Content ¦ No changes needed
 | Time Management | Time management | Same Content ¦ No changes needed
 | Endianness | Endianness | Same Content ¦ No changes needed
3.3 | - | Coordinate system | LESIA defines the CCD coordinated system. Necessary to check with DLR ICD
 | MEB Qualification | MEB qualification | Same Content ¦ No changes needed

## Slide 13: URD Comparison: N-FEE x F-FEE
# | DLR URD Section | LESIA URD Section | Comparison
4 | Interface Requirements | N-FEE / N-DPU interface | 
 | F-FEE / F-DPU SpaceWire Physical Interface | N-FEE / N-DPU SpaceWire physical interface | Same Content ¦ No changes needed
 | F-FEE / F-DPU Communication Protocol | N-FEE / N-DPU communication protocol | Same Content ¦ No changes needed
 | SpaceWire / RMAP Interface Configuration | SpaceWire / RMAP interface configuration | Same Content ¦ No changes needed
 | RMAP Protocol Management | RMAP protocol management | Same Content ¦ No changes needed
 | RMAP Configuration Areas | RMAP configuration areas | Same Content ¦ No changes needed
4.1 | SpaceWire Echoing Mode | RMAP echoing mode | DLR: Considering the original echoing mode definition (through Ethernet) LESIA: Considering the new echoing mode definition (through SpW)
4.2 | SpW Logging Mode | - | DLR: Considering the original logging mode definition LESIA: Considering that the logging mode was deleted from the scope of the project
5 | Timing and Synchronization Requirements | Timing and synchronization management | 
5.1 | F-FEE Timing Configuration | N-FEE timing configuration | a) DLR: Considers all syncs as “the same” (there is no Master Sync concept) LESIA: Considers a Master sync and several timing signal identifications b) Req. D2567 & L447: EP and RT values are different between both solutions c) Req. D2659 & L829:EP and RT changes by PUS were changed in LESIA r1+ delivery to line and columns delays. d) DLR requests a real data latency of 10ms in INTERACTIVE MODES

## Slide 14: URD Comparison: N-FEE x F-FEE
# | DLR URD Section | LESIA URD Section | Comparison
5.2 | Synchronization Signal | Synchronization signal | LESIA requirements regarding the need of a FN (910), EP (1064), EP config at startup (1065 & 1066 & 1067), use a N-FEE unused as a Synch Provider (1125 & 1126) are not listed by DLR
5.3 | Time Code Management | Time-code management | a) LESIA requirements 488 and 838 shall not be applicable to DLR: 488: The SpaceWire time-code sent by the SimuCam MEB shall be the same for all the links. 838: Deleted b) DLR stands that “The SimuCam MEB shall allow the user to select, via an Ethernet command, which SpaceWire link to use for time-code transmission”
 | Readout Order | - | MOVED TO ITEM 7
5.4 | Synchronization Reset | Synchronization reset | DLR establishes the presence of an auto reset mode, to be enabled and disabled by ethernet (LESIA don’t have this requirement).

## Slide 15: URD Comparison: N-FEE x F-FEE
# | DLR URD Section | LESIA URD Section | Comparison
6 | SSD Management Requirements | SSD management | 
 | SSD Storage Unit | SSD storage unit | Same Content ¦ No changes needed
 | Full image Storage Management | Fullimage storage management | Same Content ¦ No changes needed
 | Window Stack Storage Management | Window stack storage management | Same Content ¦ No changes needed
7 |  | N-FEE Digitalization simulation | 
7.1 |  | Digitalization area definition | LESIA defines a Digitalization function, where the user chooses the first and the last rows to be digitized – this is not a requirement for DLR in this URD version.
7.2 | Read out order (moved from item 5) | Read-out order | LESIA defines a Read-out order (as defined in RMAP) – this is not a requirement for DLR in this URD version.
7.3 |  | Warm-up simulation | LESIA defines a digitized parameter for N-FEE order (as defined in RMAP) – this is not a requirement for DLR in this URD version. It could have a relation with DLR’s AEB NO DATA
8 | - | N-FEE to N-DPU data packet transmission | LESIA defines DATAPACKLEN defining the length of the content of a packet used for data transmission – this is not a requirement for DLR in this URD version.
9 | - | N-FEE on mode simulation | LESIA defines an ON MODE Simulation -this is not a requirement for DLR in this URD version, but it is a requirement in DLR’s ICD.
10 | Standby Mode Simulation | N-FEE standby mode simulation | LESIA defines that all mode transitions should happen on the release of the Master Sync - this is not a requirement for DLR

## Slide 16: URD Comparison: N-FEE x F-FEE
# | DLR URD Section | LESIA URD Section | Comparison
11 | Full image Mode Simulation | N-FEE fullimage mode simulation | 
11.1 | Full image Mode Management | N-FEE fullimage mode management | a) DLR defines that SimuCam should not follow the LESIA req. 444: In the NFEE_RUNNING_FULLIMAGE and NFEE_RUNNING_FULLIMAGE_PATTERN state, the N-FEE simulation entity shall select the CCD side (right or left) to transmit according to the content of the ad-hoc RMAP command received from the N-DPU. This requirement is in line with the F-FEE ICD b) DLR fullimage mode is not considering ON Mode transition in this URD version (it is in the ICD). IMPORTANTE: ACHO QUE INDUZIMOS A LESIA NA DECISÃO DO FULLIMAGE – ELES SABIAM DAS DIFERENÇAS EM RMAP?
 | Full Image - Pattern Mode | N-FEE fullimage / pattern mode | Same Content ¦ No changes needed
 | Full image / SSD Image Mode | N-FEE fullimage / SSD image mode | Same Content ¦ No changes needed
 | Full image Interactive Mode Management | - | DLR defines an interactive mode – this is not a requirement for LESIA
 | Full image Interactive Mode | - | DLR defines an interactive mode – this is not a requirement for LESIA
 | Windowing Interactive Mode Management | - | DLR defines a windowing interactive mode – this is not a requirement for LESIA
 | Windowing Interactive Mode | - | DLR defines a windowing interactive mode – this is not a requirement for LESIA

## Slide 17: URD Comparison: N-FEE x F-FEE
# | DLR URD Section | LESIA URD Section | Comparison
12 | Windowing Mode Simulation | N-FEE windowing mode simulation | 
12.1 | Windowing Mode Management | N-FEE windowing mode management | DLR data transmission: 325 36-pixel star windows plus 100 16-pixel background windows (TBC) OLN overscan lines (which contains the smearing data and offset data (TBC)) LESIA data transmission: 41314 36-pixel windows OLN overscan lines (which contains the smearing data)
12.2 | Window List Management | Window list management | DLR amount of windows: 325 36-pixel star windows plus 100 16-pixel background windows (TBC) LESIA data transmission: 41314 36-pixel windows
12.3 | - | Packet order list management | LESIA defines a packet order list management -this is not a requirement for DLR in this URD version
 | Windowing / Pattern Mode | N-FEE windowing / pattern mode | Same Content ¦ No changes needed
 | Windowing / SSD Image Mode | N-FEE windowing / SSD image mode | Same Content ¦ No changes needed
 | Windowing / SSD Window Mode | N-FEE windowing / SSD window mode | Same Content ¦ No changes needed
12.4 | Windowing Interactive Mode Management | - | DLR defines a windowing interactive mode – this is not a requirement for LESIA
12.5 | Windowing Interactive Mode | - | DLR defines a windowing interactive mode – this is not a requirement for LESIA

## Slide 18: URD Comparison: N-FEE x F-FEE
# | DLR URD Section | LESIA URD Section | Comparison
13 |  | N-FEE Trap pumping mode simulation | LESIA defines a Trap Pumping mode – this is not a requirement for DLR in this URD version, and it is not a requirement in the ICD 0007 D3
14 |  | N-FEE Immediate ON command simulation | LESIA defines a immediate ON mode – this is not a requirement for DLR in this URD version In DLR ICD 0007 D3 we have a Immediate Standby mode.
15 | Transparent Mode Requirements | - | 
15.1 | Transparent Mode Management | - | DLR defines a TRANSPARENT mode in which it receives packets via EDEN and directly transmits them via one of the SpaceWire channels to the F-DPU. This is not a requirement to LESIA.
15.2 | Transparent Mode | - | DLR defines a TRANSPARENT mode in which it receives packets via EDEN and directly transmits them via one of the SpaceWire channels to the F-DPU. This is not a requirement to LESIA.
16 | Housekeeping Requirements | N-FEE housekeeping simulation | LESIA defines the need to have the frame number register in the HK parameters to be managed. This is not a requirement for DLR. Also the core of the HK data is different between both solutions
17 | - | N-FEE configuration simulation | LESIA defines the expected minimum RMAP configuration for the SimuCam – this is not a requirement for DLR in this URD version, but it is defined in the ICD 0007 D3
18 | - | RMAP register simulation | LESIA defines the expected minimum RMAP configuration for the SimuCam – this is not a requirement for DLR in this URD version, but it is defined in the ICD 0007 D3

## Slide 19: URD Comparison: N-FEE x F-FEE
# | DLR URD Section | LESIA URD Section | Comparison
19 | Error Injection Requirements | Error injection | 
 | Error Injection Management | Error injection management | Same Content ¦ No changes needed
 | SpaceWire Errors | SpaceWire errors | Same Content ¦ No changes needed
 | RMAP Errors | RMAP errors | Same Content ¦ No changes needed
 | Time-Code Errors | Time-code errors | Same Content ¦ No changes needed
 | Full image Transmission Errors | Fullimage transmission errors | Same Content ¦ No changes needed
 | Window Transmission Errors | Window transmission errors | Same Content ¦ No changes needed
19.1 |  | Image and Window content errors | LESIA defines the errors for Image and Window content – this is not a requirement for DLR in this URD version
19.2 |  | Data packet header error | LESIA defines the errors for data package header – this is not a requirement for DLR in this URD version
20 | Status / Event / Log Reporting Requirements | Status / event / log reporting | 
20.1 | Status Reporting | Status reporting | MEB global status info are different between LESIA and DLR
 | Event Reporting | Event reporting | Same Content ¦ No changes needed
 | Log Reporting | Log reporting | Same Content ¦ No changes needed
21 |  | Quality Requirements | LESIA defines need to have a uniquely identification and a name Neededntion for SimuCam– this is not a requirement for DLR in this URD version

## Slide 20: URD Conclusions

## Slide 21: Conclusions
# | Section | Discrepancy | Risk Evaluation | Component(s) Impacted | Actions Needed
3.1 | MEB Communication Interface | DLR: Establishes the Services that should be implemented. Needs to be evaluated, but should not be a problem, as the PUS DB is defined by DLR, reviewed by IMT and forwarded to LESIA. | Low (If a PUS command is mandatory to DLR but not implemented to LESIA we could have missing commands for F-FEE) | NUC (T. Ricciardi) SW (R. Napoli) | E.Marques: Compare the PUS DB and the DLR URD checking if we have any discrepancy If needed: T. Ricciardi: Implement the new commands R. Napoli: Implement the new functions related with the new commands
3.2 | F-FEE Emulation Entities | DLR: SimuCam should manage 2 F-FFE ¦ 4 SpW links associated to 1 F-FEE F-FEE states: FFEE_CONFIG; FFEE_RUNNING_STANDBY;FFEE_RUNNING_IMAGE ; FFEE_RUNNING_WINDOW ; FFEE_RUNNING_IMAGE_INTERACTIVE; FFEE_RUNNING_WINDOW_INTERACTIVE ; FFEE_RUNNING_IMAGE_TEST ; FFEE_RUNNING_WINDOW_TEST LESIA: SimuCam should manage 6 N-FEE ¦ 1 SpW links associated to 1 F-FEE N-FEE states: NFEE_CONFIG; NFEE_RUNNING_ON; NFEE_RUNNING_STANDBY; NFEE_RUNNING_FULLIMAGE; NFEE_RUNNING_WINDOWING; NFEE_RUNNING_FULLIMAGE_PATTERN; ; NFEE_RUNNING_WINDOWING_PATTERN; NFEE_RUNNING_PARALLEL_TRAP_PUMP_1; NFEE_RUNNING_PARALLEL_TRAP_PUMP_2; NFEE_RUNNING_SERIAL_TRAP_PUMP_1; NFEE_RUNNING_SERIAL_TRAP_PUMP_2 | Medium (F-FEE and N-FEE states should be related, and by now even in the ICD we don’t see this relation. LESIA’s Mode ON and Trap Pump Modes are not represented in DLR’s definition) | SW (R. Napoli) NUC (T. Ricciardi) | E. Marques: Open a JIRA and confirm this discrepancy with DLR If needed: R. Napoli: Change the F-FEE state machine to operate without the modes requested by LESIA (important: This SW change was implemented in R1+ SW released) T. Ricciardi: Generate a new SimuPUS version considering only the active commands

## Slide 22: Conclusions
# | Section | Discrepancy | Risk Evaluation | Component(s) Impacted | Actions Needed
3.3 | Coordinate system | LESIA defines the CCD coordinated system. Necessary to compare with DLR documentation | Low (I couldn’t find the same info for DLR, but by history it should be the same) | SW (R. Napoli) NUC (T. Ricciardi) HW (A. Deucher) | E.Marques: Check the information with DLR spec.
4.1 | SpaceWire Echoing Mode / RMAP Echoing Mode | DLR: Considering the original echoing mode definition (through Ethernet) LESIA: Considering the new echoing mode definition (through SpW) | Medium (If DLR disagree with this solution, a new implementation should be considered) | SW (R. Napoli) NUC (T. Ricciardi) HW (A. Deucher) | E.Marques: Open a JIRA and discuss this new scenario with DLR If needed: R. Napoli/T. Ricciardi/A. Deucher: Generate the design and implement this feature
4.2 | SpW Logging Mode | DLR: Considering the original logging mode definition LESIA: Considering that the logging mode was deleted from the scope of the project | Medium (If DLR disagree with this solution, a new implementation should be considered) | SW (R. Napoli) NUC (T. Ricciardi) HW (A. Deucher) | E.Marques: Open a JIRA and discuss this new scenario with DLR If needed: R. Napoli/T. Ricciardi/A. Deucher: Generate the design and implement this feature
5.1 | N/F-FEE Timing Configuration | a) DLR: Considers all syncs as “the same” (there is no Master Sync concept) LESIA: Considers a Master sync and several timing signal identifications b) Req. D2567 & L447: EP and RT values are different between both solutions c) Req. D2659 & L829:EP and RT changes by PUS were changed in LESIA r1+ delivery to line and columns delays. d) DLR requests a real data latency of 10ms in INTERACTIVE MODES | a) High (this difference impacts on the core of Tiago’s solution, as we have the Master Sync and the Pre Sync “entities” as the base of N-FEE’s state machine operation) b) Low (parameters set by SD card, and could be changed by the user) c) Medium(If DLR disagree with this solution, a new implementation should be considered) d) High (Interactive modes are exclusive for DLR application, and this latency is critical to SimuCam) | SW (R. Napoli) HW (A. Deucher) | a) R. Napoli/A. Deucher: Change Pre Sync/Master Sync logic in order to work with the syncs b) E.Marques: Open a JIRA and discuss this new scenario with DLR c) E.Marques: Open a JIRA and discuss this new scenario with DLR d) R. Napoli/A. Deucher: Generate the design and implement this feature

## Slide 23: Conclusions
# | Section | Discrepancy | Risk Evaluation | Component(s) Impacted | Actions Needed
5.2 | Synchronization Signal | LESIA requirements regarding the need of a FN (910), EP (1064), EP config at startup (1065 & 1066 & 1067), use a N-FEE unused as a Synch Provider (1125 & 1126) are not listed by DLR | Medium (This is a specific requirement from LESIA, and is necessary to check if they will want something like that) | SW (R. Napoli) | SHOULD WE ASK DLR? E.Marques: Confirm with DLR if this feature will be implemented for F-FEE.
5.3 | Time Code Management | a) LESIA requirements 488 and 838 shall not be applicable to DLR: 488: The SpaceWire time-code sent by the SimuCam MEB shall be the same for all the links. 838: Deleted b) DLR stands that “The SimuCam MEB shall allow the user to select, via an Ethernet command, which SpaceWire link to use for time-code transmission” | a) Low (It is a constraint of the F-FEE definition) b) Medium (Necessary to check if this PUS is already implemented. If so, the SW change doesn’t seem to be hard – necessary to direct the source of the Time-Code) | a) NA b) SW (R. Napoli) NUC (T. Ricciardi) | a) NA b) E. Marques: Check with T. Ricciardi and with T. Sanches if the SW is ready for this implementation. R. Napoli: Insert a “Time Code source” selection related with the PUS command correspondent
5.4 | Synchronization reset | DLR establishes the presence of an auto reset mode, to be enabled and disabled by ethernet (LESIA don’t have this requirement). | Medium (necessary to comprehend the impacts of it in DLR solution | SW (R. Napoli) | E.Marques: Confirm how this feature should be implemented an the impcts on LESIA SW
7.1 | Digitalization area definition | LESIA defines a Digitalization function, where the user chooses the first and the last rows to be digitized – this is not a requirement for DLR in this URD version. | Low (Necessary to check with DLR if this feature should be implemented. If so, it is already implemented for LESIA. Important to remember that this scenario is not defined even in DLR ICD) | SW (R. Napoli) | E.Marques: Confirm with DLR if this feature will be implemented for F-FEE. If NOT needed: R.Napoli: Disable this portion of the SW or check the impacts to live with it (with no activation)

## Slide 24: Conclusions
# | Section | Discrepancy | Risk Evaluation | Component(s) Impacted | Actions Needed
7.2 | Read-out order | LESIA defines a Read-out order (as defined in RMAP) – this is not a requirement for DLR in this URD version. | Low (Necessary to check with DLR if this feature should be implemented. If so, it is already implemented for LESIA. There are some mentions to it in the ICD) | SW (Napoli) | E.Marques: Confirm with DLR if this feature will be implemented for F-FEE. If NOT needed: R.Napoli: Disable this portion of the SW or check the impacts to live with it (with no activation)
7.3 | Warm-up simulation | LESIA defines a digitized parameter for N-FEE order (as defined in RMAP) – this is not a requirement for DLR in this URD version. It could have a relation with DLR’s AEB NO DATA | Low (Necessary to check with DLR if this feature should be implemented. If so, it is already implemented for LESIA. | SW (Napoli) | E.Marques: Confirm with DLR if this feature will be implemented for F-FEE. If NOT needed: R.Napoli: Disable this portion of the SW or check the impacts to live with it (with no activation)

## Slide 25: Conclusions
# | Section | Discrepancy | Risk Evaluation | Component(s) Impacted | Actions Needed
8 | N-FEE to N-DPU data packet transmission | LESIA defines DATAPACKLEN defining the length of the content of a packet used for data transmission – this is not a requirement for DLR in this URD version. | Low (The packet length is defined in the SD card for both applications, but it is not listed in DLR ICD) | NA | NA
9 | N-FEE on mode simulation | LESIA defines an ON MODE Simulation -this is not a requirement for DLR in this URD version, but it is a requirement in DLR’s ICD. | High (N-FEE and F-FEE modes should be well defined) | SW (Napoli) HW (Alex) NUC (Thiago) | E.Marques: Confirm with DLR the final state machine for the F-FEE If NOT needed: R.Napoli: Disable this portion of the SW or check the impacts to live with it (with no activation of the modes)
10 | N-FEE standby mode simulation | LESIA defines that all mode transitions should happen on the release of the Master Sync - this is not a requirement for DLR | High (This difference impacts on the core of Tiago’s solution, as we have the Master Sync and the Pre Sync “entities” as the base of N-FEE’s state machine operation) | SW (R. Napoli) HW (A. Deucher) | R. Napoli/A. Deucher: Change Pre Sync/Master Sync logic in order to work with the syncs
11.1 | N-FEE fullimage mode management | a) DLR defines that SimuCam should not follow the LESIA req. 444: In the NFEE_RUNNING_FULLIMAGE and NFEE_RUNNING_FULLIMAGE_PATTERN state, the N-FEE simulation entity shall select the CCD side (right or left) to transmit according to the content of the ad-hoc RMAP command received from the N-DPU. This requirement is in line with the F-FEE ICD b) DLR fullimage mode is not considering ON Mode transition in this URD version (it is in the ICD). IMPORTANTE: ACHO QUE INDUZIMOS A LESIA NA DECISÃO DO FULLIMAGE – ELES SABIAM DAS DIFERENÇAS EM RMAP? | High (N-FEE and F-FEE modes should be well defined) | SW (Napoli) HW (Alex) NUC (Thiago) | E.Marques: Confirm with DLR the final state machine for the F-FEE If NOT needed: R.Napoli: Disable this portion of the SW or check the impacts to live with it (with no activation of the modes)
12.1 | N-FEE windowing mode management | DLR data transmission: 325 36-pixel star windows plus 100 16-pixel background windows (TBC) OLN overscan lines (which contains the smearing data and offset data (TBC)) LESIA data transmission: 41314 36-pixel windows OLN overscan lines (which contains the smearing data) | Low (Only informative – current machine could handle both conditions) | NA | NA

## Slide 26: Conclusions
# | Section | Discrepancy | Risk Evaluation | Component(s) Impacted | Actions Needed
12.2 | Window list management | DLR amount of windows: 325 36-pixel star windows plus 100 16-pixel background windows (TBC) LESIA data transmission: 41314 36-pixel windows | Low (Only informative – current machine could handle both conditions) | NA | NA
12.3 | Packet order list management | LESIA defines a packet order list management -this is not a requirement for DLR in this URD version | Low (Already implemented for LESIA) | SW (Napoli) | E.Marques: Confirm with DLR if this feature will be implemented for F-FEE. If NOT needed: R.Napoli: Disable this portion of the SW or check the impacts to live with it (with no activation)
12.4 | Windowing Interactive Mode Management | DLR defines a windowing interactive mode – this is not a requirement for LESIA | High (Exclusive feature for F-FEE) | SW (Napoli) HW (Alex) NUC (Thiago) | R. Napoli/A. Deucher: Generate the design and implement this feature
12.5 | Windowing Interactive Mode | DLR defines a windowing interactive mode – this is not a requirement for LESIA | High (Exclusive feature for F-FEE) | SW (Napoli) HW (Alex) NUC (Thiago) | R. Napoli/A. Deucher: Generate the design and implement this feature
13 | N-FEE Trap pumping mode simulation | LESIA defines a Trap Pumping mode – this is not a requirement for DLR in this URD version, and it is not a requirement in the ICD 0007 D3 | Low (Already implemented for LESIA | SW (Napoli) | E.Marques: Confirm with DLR if this feature will be implemented for F-FEE. If NOT needed: R.Napoli: Disable this portion of the SW or check the impacts to live with it (with no activation)

## Slide 27: Conclusions
# | Section | Discrepancy | Risk Evaluation | Component(s) Impacted | Actions Needed
14 | N-FEE Immediate ON command simulation | LESIA defines a immediate ON mode – this is not a requirement for DLR in this URD version In DLR ICD 0007 D3 we have a Immediate Standby mode. | Low (Already implemented for LESIA | SW (Napoli) | E.Marques: Confirm with DLR if this feature will be implemented for F-FEE. If NOT needed: R.Napoli: Disable this portion of the SW or check the impacts to live with it (with no activation)
15.1 | Transparent Mode Management | DLR defines a TRANSPARENT mode in which it receives packets via EDEN and directly transmits them via one of the SpaceWire channels to the F-DPU. This is not a requirement to LESIA. | High (Exclusive feature for F-FEE) | SW (Napoli) HW (Alex) NUC (Thiago) | E.Marques: Confirm with DLR if this feature will be implemented for F-FEE. If needed: R.Napoli: Generate the design and implement this feature
15.2 | Transparent Mode | DLR defines a TRANSPARENT mode in which it receives packets via EDEN and directly transmits them via one of the SpaceWire channels to the F-DPU. This is not a requirement to LESIA. | High (Exclusive feature for F-FEE) | SW (Napoli) HW (Alex) NUC (Thiago) | E.Marques: Confirm with DLR if this feature will be implemented for F-FEE. If needed: R.Napoli: Generate the design and implement this feature

## Slide 28: Conclusions
# | Section | Discrepancy | Risk Evaluation | Component(s) Impacted | Actions Needed
16 | N-FEE housekeeping simulation | LESIA defines the need to have the frame number register in the HK parameters to be managed. This is not a requirement for DLR. Also the core of the HK data is different between both solutions | Low (Minor change in the SW, if needed) | SW (Napoli) | R. Napoli: Minor SW change
17 | N-FEE configuration simulation | LESIA defines the expected minimum RMAP configuration for the SimuCam – this is not a requirement for DLR in this URD version, but it is defined in the ICD 0007 D3 | Low (Informative only) | NA | NA
18 | RMAP register simulation | LESIA defines the expected minimum RMAP configuration for the SimuCam – this is not a requirement for DLR in this URD version, but it is defined in the ICD 0007 D3 | Low (Informative only) | NA | NA
19.1 | Image and Window content errors | LESIA defines the errors for Image and Window content – this is not a requirement for DLR in this URD version | Low (If necessary for DLR, it will be implemented before for LESIA) | SW (Napoli) | E.Marques: Confirm with DLR if this feature will be implemented for F-FEE. If NOT needed: R.Napoli: Disable this portion of the SW or check the impacts to live with it (with no activation)
19.2 | Data packet header error | LESIA defines the errors for data package header – this is not a requirement for DLR in this URD version | Low (If necessary for DLR, it will be implemented before for LESIA) | SW (Napoli) | E.Marques: Confirm with DLR if this feature will be implemented for F-FEE. If NOT needed: R.Napoli: Disable this portion of the SW or check the impacts to live with it (with no activation)
20.1 | Status reporting | MEB global status info are different between LESIA and DLR | Low (Minor change in the SW, if needed) | SW (Napoli) | R. Napoli: Minor SW change

## Slide 29: Action list
Documentation
E. Marques: Confirm with DLR if and how the following URD items will affect DLR SimuCam version:
3.1 MEB Communication Interface
Software Adaptation
R. Napoli: Merge the LESIA R1+ release with DLR R1+ release and make it work in the current “DLR R1+” conditions
Software Implementation
A. Deucher: 5.1 d) | 12.4 | 12.5 Design and implement Interactive Mode
3.2 F-FEE Emulation Entities
3.3 Coordinate system
4.1 SpaceWire Echoing Mode / RMAP Echoing Mode
4.2 SpW Logging Mode
5.1 b) and c) N/F-FEE Timing Configuration
E. Marques: Confirm with DLR if and how the following ICD items will affect DLR SimuCam version:
AEB State Machine (should be implemented or not?)
Which RMAP commands will have a function and which will not?
A. Deucher: 5.1 a) | 10 Change N-FEE Pre-Sync/Master Sync logic in order to work with the F-FEE syncs
5.2 Synchronization Signal
5.3 Time Code Management
5.4 Synchronization reset
7.1 Digitalization area definition
7.2 Read-out order
7.3 Warm-up simulation
9 N-FEE on mode simulation
11.1 N-FEE fullimage mode management
12.3 Packet order list management
A. Deucher: 5.3 b) Insert a “Time Code source” selection for F-FEE
13 N-FEE Trap pumping mode simulation
14 N-FEE Immediate ON command simulation
ON HOLD: 15.1 | 15.2 Transparent Mode Management (waiting for LESIA implementation)
19.1 Image and Window content errors
19.2 Data packet header error
A. Deucher: 16 N-FEE housekeeping simulation
20.1 Status reporting
Inconsistency between ICD and URD state machines
State machines walkthrough is different between N-FEE and F-FEE
R. França: Update the RMAP Memory map (from 4 areas to 1 area) POSTPONED
R. Napoli: Update the SW in order to work with the new RMAP map POSTPONED
R. Napoli: Implement the real function for all the already defined RMAP commands
R. Napoli: AEB State Machine implementation
A. Deucher: DTC Update
R. Napoli: AEB NO DATA implementation (LESIA Digitise)
Obs: All the items listed here and not listed in the SW Adaptation or SW Implementation should stay On Hold
Content that I understand as feasible for end of January